Using R in production may require to schedule some R jobs. For instance, we might want to run an R script every Wednesday at 10 am and every Thursday at 3 pm. The script can be run from terminal using the Rscript command, which it makes it easy to automate everything. In Unix-like operating systems, we can use Cron to plan the execution of terminal scripts launching the R jobs.

Sometimes, an R script needs to run with different configuration settings. An option is including some code that reads from a configuration file. Then, we can automatically modify the configuration file before running the script. However, this approach may be a bit complex.

A more direct solution is specifying the scripts from the command line. commandArgs is an R function that reads all the command line arguments. In order to read and structure them into a list, we can use this function.

readTerminalArgs <- function () {
  terminal_args <- commandArgs()[-(1:5)]
  if(length(terminal_args) == 0) return(list())
  names_args <- c("", terminal_args[-length(terminal_args)])
  names_args[!grepl("^-", names_args)] <- ""
  names(terminal_args) <- gsub("^-", "", names_args)
  terminal_args <- terminal_args[grepl("^[^-]", terminal_args)]
  as.list(terminal_args)
}

Then, at the beginning of each script, we only need to run readTerminalArgs.

Let's build the script test.R including the function definition and

list_args <- readTerminalArgs()
print(list_args)

Running
Rscript test.R -arg1 a -arg2 1 e 5

The output will be

$arg1
[1] "a"

$arg2
[1] "1"

[[3]]
[1] "e"

[[4]]
[1] "5"

The first two arguments are named “arg1” and “arg2”, as specified in the terminal. The other two arguments don't have a name.

The remaining script can depend on list_args. In this way, we can easily schedule to run the same R script with different configurations. For instance, we can run Rscript test.R -arg1 a -arg2 1 on Wedsday and Rscript test.R -arg1 b -arg2 2 on Thursday

This solution is very basic and provides the base to read the arguments. Some additions can be:
- Setting defaults
- Setting the names of the unnamed arguments
- Including the option of specifying the name with a --